## Slide 1: CE 34500 – Transportation Engineering
Chapter 6: Fundamental Principals of Traffic Flow
Course outcome: Understand basic traffic stream parameters and models, traffic flow models, and queuing theory

## Slide 2: Traffic Flow Elements
Primary Elements
  Flow
  Density
  Speed
Another Element:
  Headway

## Slide 3: Traffic Flow Elements
Flow:
  Equivalent hourly rate at which vehicles pass a point on a highway during a period less than 1 hour

## Slide 4: Traffic Flow Elements
Density/Concentration (k)
  Number of vehicles traveling over a unit length of highway at an instant in time, veh/mile
Speed (u)
  Distance traveled by a vehicle during a unit of time
  Time mean speed is the arithmetic mean of the speeds of vehicles passing a point on a highway during an interval of time

## Slide 5: Time Mean Speed (TMS)
The TMS is the arithmetic mean of the speeds of vehicles passing a point on a highway during an interval of time.

## Slide 6: Space Mean Speed (SMS)
The SMS is the harmonic mean of the speeds of vehicles passing a point on a highway during an interval of time.
The TMS is always higher than SMS

## Slide 7: Traffic Flow Elements
Time Headway (h)
  Difference between the time the front of a vehicle arrives at a point on the highway and the time the front of the next vehicle arrives at that same point
  Usually expressed in seconds
Space Headway (d)
  Distance between the front of a vehicle and the front of the following vehicle
  Usually expressed in meters

## Slide 8: Time and Space Headway
Time Headway
Space Headway

## Slide 9: Traffic Flow Elements
Time-Space Diagram:

## Slide 10: Example 6.1

## Slide 11: Flow-Density Relationship
When the density on the highway is 0, the flow is also 0
As the density increases, the flow decreases
When the density reaches its maximum (jam density), the flow must be 0
Flow= Density X space mean speed

## Slide 12: Flow-Density Relationship
Flow= Density X space mean speed

## Slide 13: Example 6.2

## Slide 14: Mathematical Relationship Describing Traffic Flow
Macroscopic Approach: Considers traffic streams and develops algorithms that relate the flow to the density
  Greenshields Model: linear relationship between speed and density
  Greenberg Model: fluid-flow analogy
Model Application
  Regression Analysis: minimizing the squares of the differences between the observed and the expected values
  If a dependent variable y and an independent variable x are related by an estimated regression function: y = a + bx
Microscopic Approach (Car-Following Theory)
  Considers spacing between consecutive vehicles and speeds of individual vehicles

## Slide 15: Greenshield Model
Prove: the space mean speed at which the volume is maximum is equal to half the free mean speed.
Prove: the density at which the volume is maximum is equal to half the jam density.

## Slide 16: Example 6.3, 6.4