## Slide 1
Handouts / Materials
Worksheet_chapter 9
Class Schedule Overview
Post homework 1_solution
Post slides
Reading assignments.
Correction Exam 1: Wednesday, February 17
Traffic intern at INDOT Fort Wayne.
Extra credit- attend ASCE meeting on 2nd Monday

## Slide 2: CE 34500 – Transportation Engineering
Chapter 9: Capacity and Level of Service for Multilane Highways
Course Outcome 4: Perform level of service analysis to determine LOS for selected highway segments. [1, 2]

## Slide 4: Freeways
A freeway is a divided highway with full access control and two or more lanes in each direction
Signalized or stop-controlled, at-grade intersections and direct access to adjacent land use are not permitted
Opposing traffic is separated by a raised barrier, an at-grade median, or a raised traffic island

## Slide 5: Freeways

## Slide 6: Basic Freeway Segment

## Slide 7: Level of Service
A = Free-flow operations, vehicles completely unimpeded.
B = Reasonably free-flow conditions. Only slight impedance to maneuvers.
C = Noticeable restriction to maneuvers.
D = Speeds begin to decline. Reduction in comfort level.
E = Flows becomes unstable. Virtually no useable gaps. Facility at capacity.
F = Flow breakdown conditions. Arriving flow is greater than segment capacity.

## Slide 8: Density Ranges for each LOS

## Slide 9: Factors Affecting LOS for Freeways
Lane width
Lateral clearance
Vehicle Equivalents
Grade
Speed
Driver Population
Interchange spacing

## Slide 10: Base Conditions for Freeways
  Lane width: >= 12 ft.
  Lateral clearance: >=12ft
  Type of vehicle: passenger cars only
  Interchanges are spaced at least 2 mi apart
  Grades do not exceed 2%
  Drivers are familiar with the freeway
  Urban freeways are five lanes in each direction

## Slide 11: Equations for Freeway

## Slide 12: Example 9.4, 9.3, 9.5, 9.1, 9.2