## Slide 1: Lateral Thinking – 3 Light Bulbs
Since we are starting a new design project on digital logic today, consider how you might solve this puzzle…
There are three light bulbs controlled by three separate switches. The light bulbs are in a separate room and cannot be seen from the switches.
How can we figure out which switch controls which light, only entering the room on the right once?
A
B
C
1
2
3

## Slide 2: Lateral Thinking – 3 Light Bulbs Answer
There are three light bulbs controlled by three separate switches. The light bulbs are in a separate room and cannot be seen from the switches.
Solution:
Turn on one switch (A) and leave it on for a while
Turn that switch (A) off, then turn on a different switch (B)
Go check the bulbs
  A  off and hot to the touch
  B  on
  C  off and cool to the touch
Emphasize that there are 3 states instead of just 2 (on and off) when you use lateral thinking.

## Slide 3: Design Studio – Week 6
Today you will:
Learn the requirements and constraints for Project 2
Review digital logic circuits
Learn a technique for choosing a design from several options
Discover tools for managing project teams
Assignments:
Exercise worksheet for digital circuit design
Technical memo on project progress through conceptual design

## Slide 4: Project 2
Let’s hear from our next customer:
Digital logic circuits combine digital inputs using Boolean functions, such as AND, OR, and NOT.
While we’re used to working with logic levels of TRUE and FALSE, or perhaps their binary counterpart of 1 and 0, real electrical circuits use two distinct voltage levels (such as 5 V and 0 V).
The circuit you will need to make is being handed out to your team.
Ask
I need a digital logic circuit.

## Slide 5: Concept Review - Digital Logic Circuits
What does this circuit do? How do you even describe what it does?
Truth table
Equation
Let’s create a truth table and equation for this circuit.

## Slide 6: Concept Review - Digital Logic Circuit Answers
A | B | C | D | F
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
A | B | C | D | F
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
F = ( + B)·C + D

## Slide 7: Determining a Digital Design
Is there more than one way to construct a digital circuit?
Yes – a single truth table has multiple implementations…
Imagine
A | B | C | G
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
G = Is A ≥ B ≥ C?
G = + A + AB + ABC
G = (A+B+)(A++C)(A++)(+B+)
G = + AB
G =
Sum of products
Product of sums
Simplifying
Creative manipulation

## Slide 8: Concept Scoring – Pugh Matrix
How can we choose between different designs?
One rigorous way is called the Pugh design matrix, which assigns ratings based on each concept’s performance to selected criteria.
Remember… sometimes it’s okay not too be rigorous. A design that interests you might just be the best choice!
Plan

## Slide 9: Using the Design Matrix Approach
In general, the steps for creating and completing a design matrix are as follows:
Select the evaluation criteria (first column).
Assign weights to each criterion.
Place concepts to be evaluated in subsequent columns.
Rate each concept against the criteria, e.g. a range from 0 to 4.
Multiply each rating by the weight and sum the results.
The concept with the highest score “wins.”
Let’s create a design matrix for our four digital logic equations.
Plan

## Slide 10: Concept Scoring – Pugh Matrix
Fill out the following table as a class.
Let the students determine the weights and possibly add criteria.
For complexity, see if the students have a good way to measure it. For power, use the number of logic gates as a measure. For cost, use the number of IC chips.
Concept 1 = 8 AND, 3 OR, 6 NOT = 17 gates, 4 ICs Concept 2 = 3 AND, 8 OR, 6 NOT = 17 gates, 4 ICs Concept 3 = 2 AND, 1 OR, 2 NOT = 5 gates, 3 ICs Concept 4 = 2 NAND, 1 OR = 3 gates, 2 ICs
Plan

## Slide 11: Problems with the Design Matrix Approach
The design matrix is might be the most common method of selecting solutions in engineering (especially for students). Beware of some of the following pitfalls:
Avoid using requirements as evaluation criteria, which leads to “requirements tradeoff.” Your selected design should meet all of the requirements.
The design matrix is often viewed as objective, but subjective selection of evaluation criteria, weights, and rating ranges has an enormous impact on the end scores.
Try to include as much information as possible to fully evaluate the designs, but too many lesser criteria can outweigh one important factor.
Plan

## Slide 12: Subsystems
Breaking large designs into smaller pieces has several benefits:
Define smaller, solvable problems
Complete designs in a reasonable and predictable time
Easily assign parts of the design to different teams
Most major engineering projects are not developed all at once; they are developed in pieces. Breaking a solution into manageable chunks, or subsystems, is an important part of engineering design:
Requirements are allocated to different subsystems, making sure that each requirement is addressed by at least one subsystem
Development of subsystems may be concurrent or sequential
Plan

## Slide 13: Subsystem Example – Vehicle Subsystems
Consider the following problem with the given requirements:
Transport families to nearby destinations safely and affordably.
Requirements:
Accommodate seating for at least 6 people.
Reduce external impact force by more than 95% within the cabin.
Operate at 35 mpg fuel efficiency or better in-city.
Constraints:
Gasoline-powered passenger vehicle
Emissions standards, speed limits, roadway size, etc.

## Slide 14: Subsystem Example – Vehicle Subsystems (cont.)
Subsystem Definition:
Divide the development into two subassemblies:
Body frame (and cabin interior)
Accommodate seating for at least 6 people.
Reduce external impact force by more than 95% within the cabin.
Engine (and control system)
Operate at 35 mpg fuel efficiency or better in-city.

## Slide 15: Subsystem Example – Vehicle Subsystems (cont.)
Subsystem Definition:
Divide the development into two subassemblies:
Body frame (and cabin interior)
Accommodate seating for at least 6 people.
Reduce external impact force by more than 95% within the cabin.
Withstand impact force up to 450 kN without breaking.
Engine (and control system)
Operate at 35 mpg fuel efficiency or better in-city.
Operate at 35 mpg fuel efficiency or better in-city with full load.

## Slide 16: Design Process Example – Vehicle Subsystems (cont.)
Plan:
Because the design and performance of the engine depends on the frame specifications, the body frame subassembly will be developed first.
Prototype:
Verify maximum occupancy ≥ 6. (Original requirement)
Risk Reduction:
Identify engine compartment specifications earlier.
Model:
Verify breaking force > 450 kN. (Derived requirement)
Optimization:
Determine minimum material thickness that meets breaking force requirement.

## Slide 17: Work Breakdown
Individual designs and subsystems can be broken into smaller pieces, too. In this manner, individual team members can have independent work and tasks.
Consider the following hierarchy of workload “sizes”:
Milestone > Deliverable > Activity > Task
On the Studio website is a document of typical activities and deliverables for every design phase.
Let’s take a look.
Plan

## Slide 18: Project Schedules
Gantt charts are commonly used to track projects in industry.
Tasks and milestones are listed on the left
Dates are represented by the columns.
In this case, each column is 1 day.
Lines show the duration of the tasks
Inverted triangles show task completion dates.
Diamonds show milestones.
Triangles and diamonds are filled in as they are accomplished.
Plan

## Slide 19: Accountability for Tasks
Breaking down tasks into individual assignments can get more results from the team. This requires team members to be accountable for doing their work and submitting it in a timely way.
Even with tasks that include multiple team members, it is beneficial to have one person “champion” the task and take responsibility for getting it done.
Creating a chart of tasks, their primary owner, and their relative due dates is an important part of clearly defining each person’s role within the team.
Plan

## Slide 20: Task Tracker
The task tracker is provided to visualize team progress.
The spreadsheet automatically calculates colored priorities for uncompleted tasks (red, yellow, and green).
The example schedule and task tracker for Project 3 (as well as blank versions) are available on the website.
Plan

## Slide 21: Week 6 Assignments
Questions after Studio? Email your instructor or go to office hours.
Exercise
Complete the Week 6 worksheet handed out earlier.
Follow the directions to help uncover design possibilities for your team’s requirements for Project 2.
Write a technical memo covering the requested topics.
Submit the completed worksheet at the start of the next Studio.