## Slide 1: Congestion Management Process (CMP)
Los Angeles
Fort Wayne

## Slide 2: Top 10 congested cities in USA
Source: https://www.citylab.com/transportation/2018/02/traffics-mind-boggling-economic-toll/552488/
Congestion Costs: $305 billion in 2017

## Slide 3: Define Congestion Management Network
Urban areas with populations over 200,000 have been directed to use the Metropolitan Planning Area boundaries for the Congestion Management Network.

## Slide 4: Congestion Management Network
Congestion Management Boundary
Congestion Management Network

## Slide 5: System Performance Measures
The roadway system performance measures selected are as follows:
Percent of weekday peak hour vehicle miles traveled (VMT) with volume to capacity greater than “X” (“X” is a defined v/c threshold and can be translated to a level of service).
Total weekday peak hour vehicle miles traveled (VMT) with volume to capacity greater than “X” (“X” is a defined v/c threshold and can be translated to a level of service).

## Slide 6: Establish System Performance Standards
Highway System:
LOS | 
A | Acceptable Service Levels
B | 
C | 
D | 
E | Unacceptable service levels
F | 

## Slide 7: Lane Capacities and benchmark v/c ratios
The selected criteria indicate when congestion is approaching maximum capacities for LOS “D” and exceeding this level will result in volume to capacity ratios over 1.00.

## Slide 8: In-class Activity-3
Street | A street | B street | AM Peak Vol | PM Peak Vol | Length
Inter 469 | Maplecrest | Inter 69 | 2542 | 2522 | 2.26
Calculate AM V/C Ratio?
Is this roadway segment congested?

## Slide 9: Example V/C Ratio
Street | A street | B street | AM Peak Vol | PM Peak Vol | Length | AM V/C Ratio | PM V/C Ratio
Inter 469 | Maplecrest | Inter 69 | 2542 | 2522 | 2.26 | 0.71 | 0.7
Calculate AM V/C Ratio?
Is this roadway segment congested?

## Slide 10: Congested Roadway Segments
Green: 0.8-0.89
Yellow: 0.9-0.99
Red: 1.0+

## Slide 11: Congested Miles in Urban Area

## Slide 12: Congested Miles in Urban Area

## Slide 13: Congestion Duration
So far, AM and PM peak hour analyzed. How about beyond peak hours?
High risk for congestion issues: locations with v/c rations greater than 0.9 for multiple hours.

## Slide 14: High Risk Congestion Corridors in Fort Wayne
Macro-level Analysis
Micro-level Analysis

## Slide 15: Micro-level Analysis
Travel time and delay studies.
Intersection LOS analysis.
Safety analysis.
Corridor studies.

## Slide 16: Travel time and Delay Study, example
Using GPS Technology

## Slide 17: Comparison of 2012 and 2016 Travel Time and Delay

## Slide 18: Intersection LOS
Signalized Intersections: 197
Non-signalized: 114

## Slide 19: Intersection Analysis
Intersections that are predetermined to have a level of service “D” or less will also be evaluated to determine the number of queued vehicles that do not clear the intersection at the end of the analysis period.

## Slide 20: Congestion mitigation strategies
Access management
https://www.youtube.com/watch?v=j58siSPT6S8
Frontage/access road plans
Corridor protection plans
Transit marketing
Bicycle access
Intersection improvements
Signal timing plans
ITS
Incident management

## Slide 21: Common congestion management: toll
A toll bridge carries 5,000veh/day. The current toll is 150 cents. When the toll is increased by 25 cents, traffic volume decreases by 500 veh/day. Determine:
The amount of toll that should be charged such that revenue is maximized.
How much additional revenue will be received?