Function Development Example:  a sin function – fill in as we go through it (see lecture notes).

The MATLAB trigonometric functions expect their argument to be in radians. Write a function called sindeg that accepts an angle x in degrees and “returns” the value of the sine function.

Set Up/ Introduction				Type of Program: 	( Script	 ( Function

- Problem Statement:

Calculate the sin of an angle given in degrees

- Inputs:  (full name, variable to be used, units)

| Variable Name | Description | Units or Values | Input Source* |
| --- | --- | --- | --- |
| x | Angle measure | Degrees | Command line |

* Possible sources:  command line, file, interactive input

- Output:  (full name, variable to be used, units)

| Variable Name | Description | Units or Values | Output type* |
| --- | --- | --- | --- |
| s | Sin of angle | -1 to 1 | Command Line |

* Possible types:  command line, file, display

- Solution Steps (order of these two parts may be varied):

Perform calculation on test case(s)		  	Identify the steps/equations

(select a test case if one is not given,  avoid answers of 0 or 1)

x = 45

r = (/180 (45) = (/4

sin ((/4) = 0.707 …

x = 90

r = ((/180(90)) = (/2

sin ((/2) = 1

5.  Coding:  Write and run program (do this in MATLAB)

6.  Validation (Prove that the function is working correctly)

Test Case Check: Check the output against hand calculation

Always show the call statement used and the result returned in your problem sets

>> sindeg (45)

ans =    0.7071

>> sindeg (90)

ans =	  1.0000

Test case matches example calculation.

Test on wider cases: if necessary

This is very important in this case because this function is a very general function – pick five or six test cases for this function and see if the answers given are what you would expect.

e.g.      >> a = 0:30:360;

>> sindeg(a)

ans =

0    0.5000    0.8660    1.0000    0.8660    0.5000    0.0000   -0.5000   -0.8660   -1.0000   -0.8660   -0.5000   -0.0000

Notice values start at zero increase to 1, go back through zero, down to -1 and back to zero.  Just the pattern we would expect for a sine wave.  This adds to our confidence in this program.

# Text boxes

Steps/Equations

Convert degrees to radians:	r = (/180 x

Calculate the sin: 			sin(r)

function definition line includes:

the word “function”

followed by:   output = name(input)

function s = sindeg(x)

% function s = sindeg(x)

% Returns the sin of an angle given in degrees.

% This function is capable of handling vector inputs.

% S. Scott Moor 	January 2004

%

%  input:  x = angle in degrees

% output:  s = resulting sin

% r = angle in radians

% calculate radians

r = pi/180*x;

% calculate sin

s=sin(r);

Introductory comments that will be the help response.

Output variable used on LHS at end of function

Input variable from the function definition line used on RHS in calculations